## Slide 1: the 28BYj-48 Stepper Motor and the ULN2003 Driver
Bret Stateham
Microsoft Technical Evangelist
BretStateham.com
@BretStateham

## Slide 2: Overview
28BYJ-48 & ULN2003 Intro
Driving Methods
Groking the Gears
Next Steps

## Slide 3: Get the files…
The source files of the slides and demos for my entire IoT series here: http://aka.ms/IoTSource
Or download a .zip with the latest files: http://aka.ms/IoTZip
Finally, watch my IoT videos here: http://aka.ms/IoTVids

## Slide 4: 28BYJ-48 & ULN2003 Intro

## Slide 5: THE 28byj-48 Motor and ULN2003 Driver…

## Slide 6: What’s inside?

## Slide 7: The coils…
2 Coils, each in a “Unipolar” configuration with “Center Taps”

## Slide 8: THE TEETH…
4 Layers of 8 Teeth
One set of teeth per “Phase”
32 Teeth over all One tooth per “Step”

## Slide 9: The Rotor…
Permanent Magnet on a plastic body
The shaft is a gear with nine teeth.
The rotor slides down on a post extending from the bottom of the motor case & gets surrounded by the coils and teeth
N
S
N
S

## Slide 10: THE GEARS & SHAFT…
Overall 64:1 Gear Ratio. That means the motor rotor must turn sixty four full rotations for the outer shaft to turn once.

## Slide 11: Back Together…
First the Case, Coils, Teeth and Rotor…

## Slide 12: Back Together…
Then the Gears…

## Slide 13: Back Together…
Finally, the protective cover, Motor Shaft and final gear, and top plate!

## Slide 14: 28BYJ-48 motor electormagnetics
The 28BYJ-48 is a Unipolar Stepper Motor (as opposed to Bipolar).
With Unipolar motors, you don’t need to change the polarity of the voltages on any give lead. That means that you don’t need an H-Bridge to reverse the polarity.
The common center taps are connected to +5VDC. You then use some circuitry (the ULN2003 Array in this case) to pull the appropriate coil ends to ground to energize their respective half of the coil.
+5VDC
PULLED TO GROUND BY ULN2003
PULLED TO GROUND BY ULN2003

## Slide 15: 28BYJ-48 motor electrOmagnetics
The 28BYJ-48 is a Unipolar Stepper Motor (as opposed to Bipolar).
With Unipolar motors, you don’t need to change the polarity of the voltages on any give lead. That means that you don’t need an H-Bridge to reverse the polarity.
The common center taps are connected to +5VDC. You then use some circuitry (the ULN2003 Array in this case) to pull the appropriate coil ends to ground to energize their respective half of the coil.

## Slide 16: ULN2003 Darlington Array Driver
The ULN2003 houses an array of 7 Darlington Pairs
A Darlington Pair is basically a pair of transistors where the second transistor amplifies the output current of the first transistor.
This gives you a higher current gain than a single transistor and allows the low voltage, low current output of a microcontroller to drive the higher current stepper motor.
The board includes convenient IO and power headers, as well as coil power indicator LEDs
The ULN2003 actually supports seven input/output pairs, but the 28BYJ-48 only needs four (four phases) so only four pins are exposed.

## Slide 17: Connecting it all up…
This could be an Arduino, Raspberry Pi, Spark Core, or any other Microcontroller (MCU).
Connect IN1-IN4 on the ULN2003 board to Digital Output pins on your MCU. Use a separate power source for the motor if it needs more volts or amps than your MCU Power Supply can provide.

## Slide 18: Using a Separate power source…
This could be an Arduino, Raspberry Pi, Spark Core, or any other Microcontroller (MCU).
Connect IN1-IN4 on the ULN2003 board to Digital Output pins on your MCU. Use a separate power source for the motor if it needs more volts or amps than your MCU Power Supply can provide.

## Slide 19: Driving Methods

## Slide 20: Stepping methods
STEPS
1
2
3
4
5
6
7
8
PHASES
BLUE
PINK
YELLOW
ORANGE
WAVE DRIVE One phase at a time Simplest, but least used
BLUE
PINK
YELLOW
ORANGE
FULL STEP Two phases at a time Strongest Torque
BLUE
PINK
YELLOW
ORANGE
HALF STEP One, or two phases at a time
Smallest step angle Medium torque
METHODS

## Slide 21: WAVE DRIVING…
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize a single phase at a time. Magnetizes a single set of teeth. Rotor turns to align it’s magnetic poles with the teeth.
Simplest to understand, but has the largest angle per step, and the lowest torque.

## Slide 22: WAVE DRIVING – STEP 1
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize a single phase at a time. Magnetizes a single set of teeth. Rotor turns to align it’s magnetic poles with the teeth.
Simplest to understand, but has the largest angle per step, and the lowest torque.

## Slide 23: WAVE DRIVING – STEP 2
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize a single phase at a time. Magnetizes a single set of teeth. Rotor turns to align it’s magnetic poles with the teeth.
Simplest to understand, but has the largest angle per step, and the lowest torque.

## Slide 24: WAVE DRIVING – STEP 3
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize a single phase at a time. Magnetizes a single set of teeth. Rotor turns to align it’s magnetic poles with the teeth.
Simplest to understand, but has the largest angle per step, and the lowest torque.

## Slide 25: WAVE DRIVING – STEP 4
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize a single phase at a time. Magnetizes a single set of teeth. Rotor turns to align it’s magnetic poles with the teeth.
Simplest to understand, but has the largest angle per step, and the lowest torque.

## Slide 26: WAVE DRIVING – STEP 5
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize a single phase at a time. Magnetizes a single set of teeth. Rotor turns to align it’s magnetic poles with the teeth.
Simplest to understand, but has the largest angle per step, and the lowest torque.

## Slide 27: WAVE DRIVING – STEP 6
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize a single phase at a time. Magnetizes a single set of teeth. Rotor turns to align it’s magnetic poles with the teeth.
Simplest to understand, but has the largest angle per step, and the lowest torque.

## Slide 28: WAVE DRIVING – STEP 7
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize a single phase at a time. Magnetizes a single set of teeth. Rotor turns to align it’s magnetic poles with the teeth.
Simplest to understand, but has the largest angle per step, and the lowest torque.

## Slide 29: WAVE DRIVING – STEP 8
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize a single phase at a time. Magnetizes a single set of teeth. Rotor turns to align it’s magnetic poles with the teeth.
Simplest to understand, but has the largest angle per step, and the lowest torque.

## Slide 30: FULL STEPPING…
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize two phases at a time. Magnetizes a two adjacent set of teeth. Rotor turns to align it’s magnetic poles to the center of the two teeth (center of the mag field)
Same step angle as wave drive but the best torque and holding power.

## Slide 31: FULL STEPPING – Step 1
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize two phases at a time. Magnetizes a two adjacent set of teeth. Rotor turns to align it’s magnetic poles to the center of the two teeth (center of the mag field)
Same step angle as wave drive but the best torque and holding power.

## Slide 32: FULL STEPPING – Step 2
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize two phases at a time. Magnetizes a two adjacent set of teeth. Rotor turns to align it’s magnetic poles to the center of the two teeth (center of the mag field)
Same step angle as wave drive but the best torque and holding power.

## Slide 33: FULL STEPPING – Step 3
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize two phases at a time. Magnetizes a two adjacent set of teeth. Rotor turns to align it’s magnetic poles to the center of the two teeth (center of the mag field)
Same step angle as wave drive but the best torque and holding power.

## Slide 34: FULL STEPPING – Step 4
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Energize two phases at a time. Magnetizes a two adjacent set of teeth. Rotor turns to align it’s magnetic poles to the center of the two teeth (center of the mag field)
Same step angle as wave drive but the best torque and holding power.

## Slide 35: HALF STEPPING…
5.625° Step Angle – 64 Steps needed for a single rotor rotation of 360°
Alternate energizing one, then two phases.
Either one, or two sets of teeth are magnetized
Rotor turns to align it’s magnetic poles to the center of the magnetic field
Smallest step angle, but not as much torque as full stepping.

## Slide 36: HALF STEPPING – Step 1
5.625° Step Angle – 64 Steps needed for a single rotor rotation of 360°
Alternate energizing one, then two phases.
Either one, or two sets of teeth are magnetized
Rotor turns to align it’s magnetic poles to the center of the magnetic field
Smallest step angle, but not as much torque as full stepping.

## Slide 37: HALF STEPPING – Step 2
5.625° Step Angle – 64 Steps needed for a single rotor rotation of 360°
Alternate energizing one, then two phases.
Either one, or two sets of teeth are magnetized
Rotor turns to align it’s magnetic poles to the center of the magnetic field
Smallest step angle, but not as much torque as full stepping.

## Slide 38: HALF STEPPING – Step 3
5.625° Step Angle – 64 Steps needed for a single rotor rotation of 360°
Alternate energizing one, then two phases.
Either one, or two sets of teeth are magnetized
Rotor turns to align it’s magnetic poles to the center of the magnetic field
Smallest step angle, but not as much torque as full stepping.

## Slide 39: HALF STEPPING – Step 4
5.625° Step Angle – 64 Steps needed for a single rotor rotation of 360°
Alternate energizing one, then two phases.
Either one, or two sets of teeth are magnetized
Rotor turns to align it’s magnetic poles to the center of the magnetic field
Smallest step angle, but not as much torque as full stepping.

## Slide 40: HALF STEPPING – Step 5
5.625° Step Angle – 64 Steps needed for a single rotor rotation of 360°
Alternate energizing one, then two phases.
Either one, or two sets of teeth are magnetized
Rotor turns to align it’s magnetic poles to the center of the magnetic field
Smallest step angle, but not as much torque as full stepping.

## Slide 41: HALF STEPPING – Step 6
5.625° Step Angle – 64 Steps needed for a single rotor rotation of 360°
Alternate energizing one, then two phases.
Either one, or two sets of teeth are magnetized
Rotor turns to align it’s magnetic poles to the center of the magnetic field
Smallest step angle, but not as much torque as full stepping.

## Slide 42: HALF STEPPING – Step 7
5.625° Step Angle – 64 Steps needed for a single rotor rotation of 360°
Alternate energizing one, then two phases.
Either one, or two sets of teeth are magnetized
Rotor turns to align it’s magnetic poles to the center of the magnetic field
Smallest step angle, but not as much torque as full stepping.

## Slide 43: HALF STEPPING – Step 8
5.625° Step Angle – 64 Steps needed for a single rotor rotation of 360°
Alternate energizing one, then two phases.
Either one, or two sets of teeth are magnetized
Rotor turns to align it’s magnetic poles to the center of the magnetic field
Smallest step angle, but not as much torque as full stepping.

## Slide 44: REVERSING THE DIRECTION
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Just fire the phases in reverse order!
Here, we’ll use a reverse Wave Drive example…

## Slide 45: WAVE DRIVING in REVERSE – STEP 1
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Just fire the phases in reverse order!
Here, we’ll use a reverse Wave Drive example…

## Slide 46: WAVE DRIVING in REVERSE – STEP 2
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Just fire the phases in reverse order!
Here, we’ll use a reverse Wave Drive example…

## Slide 47: WAVE DRIVING in REVERSE – STEP 3
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Just fire the phases in reverse order!
Here, we’ll use a reverse Wave Drive example…

## Slide 48: WAVE DRIVING in REVERSE – STEP 4
11.25° Step Angle – 32 Steps needed for a single rotor rotation of 360°
Just fire the phases in reverse order!
Here, we’ll use a reverse Wave Drive example…

## Slide 49: Groking the Gears

## Slide 50: 64:1 Gear Ratio…
32 / 9 = 3.555
22 / 11 = 2.000
26 / 9 = 2.888
31 / 10 = 3.100
Multiply the gear ratios together: 3.555 x 2.000 x 2.888 x 3.100 = 63.65 Round 63.65 up:
64
That gives us a 64:1 gear ratio over all
It will take 64 full rotations of the “Rotor Shaft” to get 1 rotation of the “Keyed Motor Shaft”
Gear Ratios:
Keyed Motor Shaft
Rotor Shaft

## Slide 51: 64:1 Gear Ratio…
32 / 9 = 3.555
22 / 11 = 2.000
26 / 9 = 2.888
31 / 10 = 3.100
Multiply the gear ratios together: 3.555 x 2.000 x 2.888 x 3.100 = 63.65 Round 63.65 up:
64
That gives us a 64:1 gear ratio over all
It will take 64 full rotations of the “Rotor Shaft” to get 1 rotation of the “Keyed Motor Shaft”
Gear Ratios:
Keyed Motor Shaft
Rotor Shaft

## Slide 52: Gears effect on motor shaft steps
When full stepping, It takes 32 steps for the magnetic rotor inside the motor to complete a full 360° rotation, turning 11.25° each step. Half stepping changes that to 64 steps of 5.625° each for a full rotation.
The rotor shaft has a 64:1 ratio with the motor shaft though, so for the motor shaft, those numbers change to:
Full Stepping:
32*64 = 2048 Steps per motor shaft rotation
11.25° / 64 = .18° step angle
Half Stepping:
64*64 = 4096 Steps per motor shaft rotation
5.625° / 64 = .09° step angle
Keyed Motor Shaft
Rotor Shaft

## Slide 53: Next Steps

## Slide 54: Stay tuned for more videos…
I’ll follow up with videos for driving the 28BYJ-48 & ULN2003 using:
Raspberry Pi
Arduino
Possibly others

## Slide 55: Resources
Check out Tom Igoe’s notes on Stepper Motors: http://www.tigoe.net/pcomp/code/circuits/motors/stepper-motors/
Douglas W. Jones has a more technical overview: http://homepage.cs.uiowa.edu/~jones/step/
Do an internet search for the 28BYJ-48 and the microcontroller of your choice

## Slide 56: REVIEW
28BYJ-48 & ULN2003 Intro
Driving Methods
Groking the Gears
Next Steps

## Slide 57: 28BYJ-48 Gear Assembly

## Slide 58: IoT Logo

## Slide 59: arduino

## Slide 60: GALILEO BOARD

## Slide 61: LEDs

## Slide 62: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 63: cables

## Slide 66: Micro SD Cards
Font: Segoe UI Semibold