## Slide 1: Getting Started with Windows on the Intel Galileo
Bret Stateham
Microsoft Technical Evangelist
bretstateham.com
@BretStateham

## Slide 2: Overview
Windows Developer Program for IoT
Installing Windows on Galileo
Running Code
In Windows
Next Steps

## Slide 3: Get the files…
The source files of the slides and demos for my entire IoT series here: http://aka.ms/IoTSource
Or download a .zip with the latest files: http://aka.ms/IoTZip
Finally, watch my IoT videos here: http://aka.ms/IoTVids

## Slide 4: Windows Developer Program for IoT

## Slide 5: Windowsondevices.com
http://windowsondevices.com/

## Slide 6: More than just galileo…
http://aka.ms/msmb
http://aka.ms/msscb

## Slide 7: Windows compatible hardware development boards…
http://aka.ms/wchdb
http://aka.ms/wchdblive

## Slide 8: Installing windows on galileo

## Slide 9: Here’s the hardware you need…

## Slide 10: Gen 2 boards are NOT supported (yet)…
The embedded team hasn’t made any announcements or promises, but I hope to see support for the Gen 2 boards in the future.

## Slide 11: Ensure your firmware is updated
http://youtu.be/zUZmWe8nrc4

## Slide 12: Install visual studio 2013…
Can use Visual Studio Express 2013 for Windows Desktop or a full version of Visual Studio http://visualstudio.com/downloads/

## Slide 13: Install the telnet client…
You’ll use telnet to communicate with your Galileo. A telnet client ships with Windows, but isn’t installed by default. You‘ll need to add it manually…

## Slide 14: Download the windows image and tools…
https://connect.microsoft.com/windowsembeddedIoT/Downloads
Download | Description
Windows Developer Program for IoT – Microsoft Installer (MSI) | Installs Visual Studio project templates and GalileoWatcher.exe on your PC
Windows Developer Program For IoT – Windows Image (WIM) | The actual windows image that will be applied to the SD Card
Windows Developer Program For IoT – apply-bootmedia.cmd | The script to apply the WIM file (above) to the SD Card
You must have completed the registration process on windowsondevices.com before you can download

## Slide 15: Install the windows image on your sd card…
C:\Galileo>apply-BootMedia.cmd -destination d:\ -image 9600.16384.x86fre.winblue
_rtm_iotbuild.140731-1000_galileo_v1.wim -hostname mygalileo -password admin
C:\Galileo>rem *****************************************************************
*********
C:\Galileo>rem ** Copyright (c) Microsoft Open Technologies, Inc. All rights re
served.
C:\Galileo>rem ** Licensed under the BSD 2-Clause License.
C:\Galileo>rem ** See License.txt in the project root for license information.
C:\Galileo>rem *****************************************************************
*********
**** Temporary changing time zone to 'Pacific Standard Time'
**** Fat32 is local time based, and the images are created in a pacific time zon
e. If there is a mismatch Windows will bug check after 5 minutes.
**** Set-up work folder: C:\Users\Bret\AppData\Local\Temp\apply-BootMedia-22943
**** Retrieveing C:\Galileo\9600.16384.x86fre.winblue_rtm_iotbuild.140731-1000_g
alileo_v1.wim
**** to C:\Users\Bret\AppData\Local\Temp\apply-BootMedia-22943
Deployment Image Servicing and Management tool
Version: 6.3.9600.17031
Mounting image
[==========================100.0%==========================]
The operation completed successfully.
**** Customizing image C:\Users\Bret\AppData\Local\Temp\apply-BootMedia-22943\96
00.16384.x86fre.winblue_rtm_iotbuild.140731-1000_galileo_v1.wim
**** mounted at C:\Users\Bret\AppData\Local\Temp\apply-BootMedia-22943\96
00.16384.x86fre.winblue_rtm_iotbuild.140731-1000_galileo_v1.wim.mount
Deployment Image Servicing and Management tool
Version: 6.3.9600.17031
Saving image
[==========================100.0%==========================]
Unmounting image
[==========================100.0%==========================]
The operation completed successfully.
**** Applying image C:\Users\Bret\AppData\Local\Temp\apply-BootMedia-22943\9600.
16384.x86fre.winblue_rtm_iotbuild.140731-1000_galileo_v1.wim
**** to d:\
Deployment Image Servicing and Management tool
Version: 6.3.9600.17031
Applying image
[==========================100.0%==========================]
The operation completed successfully.
**** Mounting d:\\Windows\System32\config\SYSTEM
**** to HKEY_USERS\Galileo-22943-SYSTEM
**** Setting hostname to mygalileo
**** Restoring time zone to 'Pacific Standard Time'
****
**** Successfully applied C:\Galileo\9600.16384.x86fre.winblue_rtm_iotbuild.14
0731-1000_galileo_v1.wim
**** to d:\
****
**** hostname: mygalileo
**** timezone: Pacific Standard Time
**** Username: Administrator
**** Password: admin
****
**** Done.
C:\Galileo>
efi
Program Files
Tools
Users
Windows
apply-BootMedia.cmd
*.wim
C:\Galileo
D:\
Remember these values. You’ll use them to connect to your Galileo

## Slide 16: Creating a Windows Boot Image for Galileo

## Slide 17: Boot galileo to windows…
SD IO Light Will Flicker
You’ll receive a 169.254.*.* IPv4 address on both ends by default if you connect them directly (learn more)
The entire boot process can take as long as two minutes

## Slide 18: Run GalileoWatcher.exe on pC…
Installed as part of the: Windows Developer Program for IoT – Microsoft Installer (MSI)

## Slide 19: Galileo UDP multicasts…
hostname
IP Address

## Slide 20: telnet into your galileo…
User name: Administrator Password: <Whatever you used in the apply-BootMedia.cmd execution> (admin)
Administrator
admin

## Slide 21: Browse to your galileo…
http://<your galileo hostname> or http://<your galileo ip addr>
“task list” shows a list of the running processes on your Galileo
“file list” hasn’t worked for me yet.
“memory statistics” shows your current memory status

## Slide 22: Booting to Windows on your Galileo

## Slide 23: Running code in windows

## Slide 24: Galileo-sdk C++ wiring API implementation
https://github.com/ms-iot/galileo-sdk

## Slide 25: Galileo wiring app C++ project template
Installed as part of the: Windows Developer Program for IoT – Microsoft Installer (MSI)
It is basically a C++ console app that has references to the Galileo-SDK (Wiring API) to allow it to talk to the Arduino side of things.

## Slide 26: Main.cpp

## Slide 27: Default sketch
// Main.cpp : Defines the entry point for the console application.
//
#include "stdafx.h"
#include "arduino.h"
int _tmain(int argc, _TCHAR* argv[])
{
return RunArduinoSketch();
}
int led = 13; // This is the pin the LED is attached to.
void setup()
{
// TODO: Add your code here
pinMode(led, OUTPUT); // Configure the pin for OUTPUT so you can turn on the LED.
}
// the loop routine runs over and over again forever:
void loop()
{
// TODO: Add your code here
digitalWrite(led, LOW); // turn the LED off by making the voltage LOW
Log(L"LED OFF\n"); // write to stdout and to debugger if attached
delay(1000); // wait for a second
digitalWrite(led, HIGH); // turn the LED on by making the voltage HIGH
Log(L"LED ON\n"); // write to stdout and to debugger if attached
delay(1000); // wait for a second
}
The Log() method writes output to stdout and to the debugger if it is attached

## Slide 28: Remote debugging on your galileo…

## Slide 29: Writing code on your Galileo

## Slide 30: Next steps

## Slide 31: Resources and code on github…
http://ms-iot.github.io/content/IBoughtAGalileo.htm
https://github.com/ms-iot

## Slide 32: Explore other samples…
http://ms-iot.github.io/content/SampleApps.htm
The //build/ piano demo
GPIO Direct
16X2 LCD
Communication and control with Firmata and Cylon
More to come!

## Slide 33: Advanced Usage…
http://ms-iot.github.io/content/AdvancedUsage.htm
Connecting to your Galileo
Configuring Remote Debugging
Running a sketch on boot
Troubleshooting, etc.

## Slide 34: Watch other videos in the series…
http://aka.ms/iotvids

## Slide 35: Get the files…
The source files of the slides and demos for my entire IoT series here: http://aka.ms/IoTSource
Or download a .zip with the latest files: http://aka.ms/IoTZip
Finally, watch my IoT videos here: http://aka.ms/IoTVids

## Slide 36: REVIEW
Windows Developer Program for IoT
Installing Windows on Galileo
Running Code
In Windows
Next Steps

## Slide 37: IoT Logo

## Slide 38: arduino

## Slide 39: GALILEO BOARD

## Slide 40: LEDs

## Slide 41: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 42: USB and power cables