## Slide 1: Getting Started with the Intel Galileo
Bret Stateham
Microsoft Technical Evangelist
bretstateham.com
@BretStateham

## Slide 2: Overview
Intro to the Galileo
Setting up your Galileo
Running your first Sketch
Next Steps

## Slide 3: Intro to the Intel Galileo

## Slide 4: Intel Galileo overview
“Arduino Certified” board
Uses Intel Quark SOC w/ 256MB RAM
Arduino UNO R3 Pin Compatible
Has connections for….
  Ethernet
  RS232 3.5mm jack
  USB Client (connect to pc)
  USB Host (connect to peripheral)
  Mini PCI Express on the back
Runs Linux by default
Can boot other OSs from SD Card

## Slide 5: Where can you get one?
Generation 1 (Gen 1) boards now seem to be readily available
Multiple Online sources sell them for around $50-$80 USD…

## Slide 6: Galileo gen 2 boards (not covered in this session)
RS232 connection is now a 6-pin header replaces vs the 3.5mm jack.
The USB Host connection uses a full size connector
12-bit pulse-width modulation (PWM) precision
Serial input can be redirected to the Arduino to reduce the need for SoftwareSerial
12V Power-over-Ethernet (PoE) capable
Power regulation system changed to accept power supplies from 7V to 15V.

## Slide 7: Learn more
https://communities.intel.com/community/makers

## Slide 8: First look at the Intel Galileo

## Slide 9: Setting up your Galileo

## Slide 10: What’s in the box
Intel Galileo
5V Power Supply and Cable

## Slide 11: What’s not in the box?
There isn’t a Micro USB cable included in the box. You’ll need to supply one yourself to connect your PC to your Galileo

## Slide 12: DOWNLOAD the software
https://communities.intel.com/docs/DOC-22226

## Slide 13: Unblock the .zip file
Windows “Blocks” files downloaded from the Internet.
Before you extract the .zip file, “Unblock” it first to prevent security errors later.

## Slide 14: Extract .ZIP TO THE ROOT
If you don’t extract to the root (or to a path close to the root) you could exceed the maximum path length
If you already have a copy of the Arduino IDE installed, make sure to extract this to a different path.
You can have multiple versions of the Arduino IDE on the same machine by simply extracting the .zip to a different location

## Slide 15: Connect to power and usb
Make sure to use the 5V power supply that was provided with your Galileo! DO NOT USE MORE THAN 5v!

## Slide 16: Install the device driver

## Slide 17: Run the Arduino IDE & SELECT GALILEO

## Slide 18: Update the Galileo's firmware

## Slide 19: Setting up your Intel Galileo

## Slide 20: Running your first sketch

## Slide 21: Processing, Wiring, Arduino & Galileo
Processing (processing.org) Was developed to help artists, etc. learn programming and use technology in their creative efforts
Wiring (wiring.org.co) Wiring built on Processing to provide a way to write code for a microcontroller
Arduino (arduino.cc) The Arduino development language and IDE is based on that of Wiring and adds specific functionality for the Arduino board as well as libraries for common hardware
Galileo (maker.intel.com) Is an “Arduino Certified” board based on an Intel processor. It allows you to develop applications using the Arduino IDE and libraries, mostly un-modified.

## Slide 22: Arduino “sketches”
Arduino programs are called “Sketches”
The “setup” method runs once at the beginning
The “loop” method is called repeatedly
Upload your sketch to the selected board to run your sketch

## Slide 23: Digital Pins
Digital Pins 0-13 and Analog pins A0-A5 allow you to read and write digital signals (LOW or HIGH)
Configure a pin for output with: pinMode(pin#,OUTPUT);
Write values with:
digitalWrite(pin#,LOW); or
digitalWrite(pin#,HIGH);
Configure a pin for input with:
pinMode(pin#,INPUT);
Read values from the pin with:
int val = digitalRead(pin#);

## Slide 24: POWER
Multiple Ground (GND) and Voltages (3.3v and 5v) can be accessed from the board.
Use these to supply ground and power to other sensors, LEDs, etc.
Make sure not to draw more amperage that the board is rated for. (800mA max across all pins - learn more

## Slide 25: Light emitting diodes (LEDs)
Long Leg
Short Leg
Small Post
Big Post
Flat Edge
Vcc (+)
GND
Anode (+)
Cathode (-)
Diodes only let current flow in one direction
They have a “polarity” which means you need to connect them the right way.
The side of the LED that is connected to the positive voltage source is called the “Anode”.
The side of the LED that is connected to ground is called the “Cathode”
With Light Emitting Diodes (LEDs), when you apply a positive voltage to the anode, the diode emits light.

## Slide 26: Fritzing.org

## Slide 27: BLINK
Anode (+) : Long Leg
Cathode (-) : Short Leg

## Slide 28: Blink – The Arduino “Hello, World!” sketch

## Slide 29: Next steps

## Slide 30: Get engaged!
maker.intel.com

## Slide 31: Run windows on YOUR Galileo
Windows Developer Program for IoT

## Slide 32: REVIEW
Intro to the Galileo
Setting up your Galileo
Running your first Sketch
Next Steps

## Slide 33: IoT Logo

## Slide 34: Arduino

## Slide 35: GALILEO BOARD

## Slide 36: LEDs

## Slide 37: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 38: USB